## Slide 1
SOFTWARE ENGINEERING LAB · PROJECT-BASED LEARNING
Smart Classroom Electricity Management System
Vacancy detection, AC-state inference and appliance control
Vineet Shah · Roll No. 28 · 5S CSE, A6-B2
Software Engineering Lab (24CS01PR0502) · 2026-27
2
modules built
78
test cases
45
Jira work items
Notes: Individual SE PBL project. The problem statement is from my Idea Lab project; for this PBL I built two software modules, managed the work in Jira and tested it with 78 test cases.

## Slide 2
Why classrooms waste electricity
1
Appliances stay ON
Lights, fans and ACs keep running after a lecture ends. Manual switching and fixed timers cannot follow irregular schedules.
2
Sensors miss the picture
PIR sensors cannot see whether fans or lights are on, and miss people who sit still.
3
AC state is invisible
One temperature sensor cannot tell whether the AC is still cooling an empty room.
Proposed system
CCTV + YOLOv8 counts people, fans and lights; four DHT11 sensors read four room regions; an ESP32 switches relays; a web dashboard shows alerts and lets an operator act.
Smart Classroom Electricity Management · SE Lab PBL · Vineet Shah
2
Notes: Problem statement from the Idea Lab project 'Electricity Management through Computer Vision & Temperature Sensing'.

## Slide 3
What this PBL builds
Implemented
Module 1 - detection engine Module 2 - REST API, SQLite database and web dashboard
Simulated
CCTV + YOLOv8, four DHT11 sensors and the ESP32 are replaced by app/simulator.py, which sends the same data
Python 3.11 standard library · SQLite · HTML, CSS, JavaScript
Smart Classroom Electricity Management · SE Lab PBL · Vineet Shah
3
Notes: Green boxes are what I implemented. The hardware and the trained model were not available, so a simulator posts the same frames and executes relay commands like the ESP32.

## Slide 4
Module 1 · Vacancy and AC-state detection engine
Vacancy
Room is vacant only after N consecutive frames with no people (default 10). Any person resets the count.
Wastage alerts
FAN_ON_VACANT and LIGHT_ON_VACANT are raised while the room is vacant, once per occurrence.
AC inference
After wait_seconds, mean temperature drop over the 4 regions >= threshold means the AC is still ON.
Smart Classroom Electricity Management · SE Lab PBL · Vineet Shah
4
Notes: app/engine.py - RoomMonitor processes one frame at a time and validates every input (counts 0-50, temperatures 0-50 deg C, increasing timestamps).

## Slide 5
Module 2 · Monitoring dashboard and control
1
Live room status
state badge, people, fans and lights ON, AC check, 2x2 heatmap
2
Alerts
open alerts listed newest first; operator acknowledges with name and remarks
3
Manual override
fan or light ON/OFF queued for the ESP32, marked done when executed
4
Settings
vacancy frames, wait time and threshold, validated and stored in SQLite
5
REST API
/api/readings, /alerts, /override, /commands, /settings
Smart Classroom Electricity Management · SE Lab PBL · Vineet Shah
5
Notes: Screenshot from the simulator run on 25-10-2026: LAB-1 left with 2 fans, 6 lights and the AC on - three open alerts and a pending fan OFF command.

## Slide 6
Managed in Jira · space SCEM
4
epics
9
user stories
10
tasks
18
subtasks
4
bugs
3
sprints
Epic -> Story / Task / Bug -> Subtask
Backlog imported from jira/jira_import.csv
Workflow: To Do -> In Progress -> Done
Each bug carries steps, severity, priority and a fix + retest comment
Smart Classroom Electricity Management · SE Lab PBL · Vineet Shah
6
Notes: Site rbunagpur-team-zhx8jd75.atlassian.net, space Smart Classroom Electricity Management (key SCEM), Scrum, team-managed. Screenshot: sprint planning in the backlog.

## Slide 7
Three sprints, tracked to Done
Sprint | Goal | Items | Points | State
SCEM Sprint 1 25-10 19:30-19:50 | Detection engine (Module 1) and requirements | 6 | 16 | Completed
SCEM Sprint 2 25-10 19:50-20:00 | Dashboard, API, database and simulator (Module 2) | 6 | 22 | Completed
SCEM Sprint 3 25-10 20:00 - 01-11 | Testing, bug fixing and documentation | 11 | 16 | Active
Sprint 3 holds the testing tasks and the four bugs; the report and presentation task stays In Progress until submission.
Smart Classroom Electricity Management · SE Lab PBL · Vineet Shah
7
Notes: Status on 26-10-2026: 43 work items Done, 2 In Progress (SCEM-23 report and presentation, and its epic SCEM-4).

## Slide 8
78 automated test cases
32
Unit tests engine
24
API tests server + DB
7
Integration end to end
15
UI tests in Edge
✓
Functional
every requirement checked through its output
✓
Equivalence partitioning
valid and invalid classes for each input
✓
Boundary value analysis
min-1, min, max, max+1 for every limit
✓
Validation
every API and form error message
✓
Unit and integration
engine alone, then engine + API + DB + ESP32 loop
Format: Test Case ID · Module · Test Scenario · Test Data · Expected Result · Actual Result · Status
Smart Classroom Electricity Management · SE Lab PBL · Vineet Shah
8
Notes: Expected results come from the requirements (docs/requirements.md), written before the first run. python -m tests.run_tests executes all cases and records the actual result of each.

## Slide 9
Run 1 found 4 real bugs
73 / 5
Run 1: passed / failed
→
78 / 0
Run 2 (retest): passed / failed
Each failure was analysed, logged as a Bug in Jira, fixed in code and retested.
Fix and retest comments are on each bug (SCEM-24 to SCEM-27).
BUG-01 · SCEM-24
Minor / Medium
Room with no readings shown as OCCUPIED
BUG-02 · SCEM-25
Major / High
False AC alert at 0.499 deg C drop (rounding)
BUG-03 · SCEM-26
Minor / Low
Missing room_id gave 404 'Room None'
BUG-04 · SCEM-27
Trivial / Low
Settings errors showed internal field names
Smart Classroom Electricity Management · SE Lab PBL · Vineet Shah
9
Notes: BUG-02 was the most serious: the mean drop was rounded to 2 decimals before the threshold comparison. Found by the BVA case threshold - 0.001.

## Slide 10
Bug fix and retest evidence · BUG-01
Before fix: OCCUPIED, TC_UI_01 FAIL
After fix: NO DATA, TC_UI_01 PASS
Same seeded data, same test case, captured from the real dashboard in Microsoft Edge before and after the fix
Smart Classroom Electricity Management · SE Lab PBL · Vineet Shah
10
Notes: The dark bar at the top of each screenshot is added by the UI test harness and shows the test case, time and result.

## Slide 11
Live demonstration
1
Start the server
python -m app.server --port 8090
2
Run the classroom simulator
python -m app.simulator --room LAB-1 --scenario ac_left_on
3
Watch and act
alerts appear; acknowledge, override a fan, change a setting
4
Run all tests
python -m tests.run_tests
CR-201 after everything was switched off: AC inferred OFF (room warmed by 0.24 deg C)
Smart Classroom Electricity Management · SE Lab PBL · Vineet Shah
11
Notes: Demo order: server, simulator scenario ac_left_on for LAB-1 (fan, light and AC alerts), acknowledge an alert, send fan OFF, then all_off for CR-201, then the test run.

## Slide 12
Conclusion and next steps
What was achieved
Two working modules with database, validation and integration
Jira project: 45 work items, 3 sprints, bugs tracked to closure
78 test cases; 4 bugs found, fixed and retested; 78 / 78 pass
Next steps
Connect the real CCTV + YOLOv8, DHT11 sensors and ESP32
MQTT between classroom node and server
Daily energy-wastage report and mobile alerts
Thank you · Questions?
Notes: Close with the results and the next steps toward the full hardware system.